## Slide 1
Predictive Modeling of Rootzone Variables Using Greenhouse Data
Students: Eden Eliyahu, Oren Chaushu Supervisors: Dr. Avner Priel - Ruppin, Dr. Alaa Jamal - Volcani Institute
Dataset
Introduction & Goal
Model / Validation
System Architecture
Methods & Workflow
Results
Conclusions
Practical Value
Problem:
pH and EC are critical indicators of nutrient availability, salinity, and plant health.
Challenge:
Manual samples are accurate but sparse, creating blind intervals.
Goal:
Predict future pH and EC up to 48h using greenhouse, irrigation, fertilization and crop data.
16,682 records
109 labeled pH/EC samples
10-min resolution
May–Sep 2025
1. Clean & synchronize data
2. Predict microclimate
3. Build t0→t1 intervals
4. Engineer features
5. Train/evaluate model
Unified model:
Same feature framework for pH and EC
hybrid logic:
Normal regime → XGBoost
High-salt / no-flush → Huber
Validation:
Chronological split
Walk-forward
Holdout skip-pairs
Naive baseline comparison
Meteorological files → Microclimate model→ Predicted greenhouse conditions→ Initial pH/EC + irrigation + fertilization + crop status → Unified Rootzone Model → Predicted pH + EC up to 48h
pH MAE ≈ 0.31–0.33
pH R² ≈ 0.93–0.94
EC MAE ≈ 0.12–0.13
EC R² ≈ 0.95–0.98
The model outperformed the naive baseline despite sparse manual labels.
A unified framework can predict both pH and EC.
Interval-based modeling bridges sparse manual samples.
Hybrid EC logic helps with unusual salinity regimes.
Estimates rootzone state between manual samples.
Supports irrigation and fertilization decisions.
Enables scenario testing for optimization.