## Slide 1
Predictive Modeling of Rootzone Variables
Using Greenhouse Data
Students: Eden Eliyahu, Oren Chaushu
Mentors: Dr. Avner Priel - Ruppin, Dr. Alaa Jamal - Volcani Institute
1
Introduction & Goal
Why rootzone monitoring needs a soft sensor.
Rootzone pH and EC are key indicators of nutrient availability, salinity, and plant health in greenhouse cultivation. Manual samples are accurate, but they are sparse - between samples, acidity or salinity changes may go undetected.
Manual
sample
Blind
interval
Rootzone
soft-sensor
prediction
Goal - Build a rootzone soft sensor that predicts future pH and EC
between manual samples to optimize irrigation and fertigation
decision-making.
2
Dataset & Processing
Five greenhouse domains synchronized into one 10-minute master dataset.
Climate conditions
temperature - humidity – radiation
Irrigation & fertigation
fertilizer - acid & salt inputs
Plant status
canopy cover - crop age - growth stage
Rootzone measurements
manual pH & EC samples
Time & history
timestamps - gaps - previous state
MASTER DATASET
10-minute
greenhouse grid
16,682
ROWS
10 min
GRAIN
109
PH LABELS
109
EC LABELS
20
COLUMNS
May-Sep
2025
!
Main data challenge:
dense greenhouse telemetry, sparse rootzone labels.
3
System Architecture & Workflow
PROJECT WORKFLOW
01
Problem
framing
02
Data
collection
03
Audit
& EDA
04
Master
dataset
05
Support
modeling
06
Feature
eng.
07
Model
building
08
Validation
09
Deployment
SYSTEM ARCHITECTURE
External Weather
Irrigation Plan
Current pH & EC
Micro-Climate Model
Predicted Internal Climate
Rootzone Model
Prediction
4
Model Development & Validation
Validation separates future testing, skipped intervals, and hybrid model behavior.
WALK-FORWARD STAIRCASE
Train 1
Test 1
Train 1-2
Test 2
Train 1-3
Test 3
SKIPPED-INTERVAL HOLDOUT
Hold out labeled intervals, then predict them later.
ROOTZONE HYBRID MODEL
Robust linear model
Gradient boosted trees
Handles extrapolation
beyond nearby manual samples.
Hybrid rootzone soft sensor
pH(t) + EC(t)
5
Results
Wide walk-forward traces from export data: actual and predicted.
pH
MAE
GAIN
EC
MAE
GAIN
pH ACTUAL VS PREDICTED - WALK-FORWARD
EC ACTUAL VS PREDICTED - WALK-FORWARD
6
Conclusions & Impact
Sparse manual measurements become actionable guidance for irrigation and fertigation decisions.
Earlier awareness
Detect pH and EC movement between manual samples.
Decision optimization
Support irrigation and fertigation timing and dosing.
Usable workflow
Automated ETL, prediction, and dashboard packaging.
Interpolates local pH/EC
movement between samples.