## Slide 1
Ruppin Academic Center | Department of Computer Science
Artificial Intelligence and Data Science Specialization
Predictive Modeling of Root-Zone Variables Using Greenhouse Data
Machine-learning soft sensor for pH and EC prediction between sparse manual measurements
Students: Eden Eliyahu, Oren Chaushu
Supervisors: Dr. Avner Priel, Dr. Alaa Jamal
Motivation
Root-zone pH controls nutrient availability; EC reflects salinity and fertilizer concentration.
Manual lab measurements are reliable, but sparse and reactive.
Continuous sensors can drift, need calibration, and may not represent the whole root zone.
Project Goal
Develop a machine-learning soft sensor that predicts root-zone pH and EC to support timely irrigation and fertigation decisions, maintain optimal root-zone conditions, and prevent salinity or pH imbalance.
Data
16,682
10-minute rows
109
pH/EC labels
20
Input features
Unified 10-minute dataset combining climate, fertigation, crop state, and manual pH/EC labels.
May 29-Sep 21, 2025 | sparse target labels
05
Method
Stage 1 predicts greenhouse microclimate from external weather and radiation.
Stage 2 predicts future root-zone pH and EC from a known anchor measurement at t0.
The model learns interval change from t0 to t1 instead of treating every timestamp as a label.
07
Support Model: Micro-Climate
06
Validation Strategy
Walk-forward validation: train only on past observations and predict future samples.
Skipped-interval holdout: remove selected target intervals from training and predict them later.
Metrics are interpreted per target: pH and EC mS/cm
08
Key Results
0.33
pH MAE
62%
pH gain
0.932
pH R2
0.127
EC MAE
35%
EC gain
0.982
EC R2
09
Conclusions
A soft sensor can estimate root-zone pH and EC despite sparse target labels.
Combining climate, fertigation, crop state and previous pH/EC improves prediction over carry-forward baselines.
The model supports earlier irrigation and fertigation decisions, not autonomous control.
10
Limitations
Only 109 labeled pH/EC measurements.
Evaluated on one growing season.
Low EC values remain difficult because small absolute errors become large relative errors.
Future work: more seasons, crops, greenhouses and online monitoring.
Climate conditions
temperature · humidity · radiation
Irrigation & fertigation
water · fertilizer · acid · salts
Plant status
canopy cover · crop age
Root-zone measurements
manual pH & EC samples
Time & history
timestamps · gaps · previous state
Estimates internal greenhouse climate from external weather and radiation.
Creates continuous climate features for the root-zone prediction model.
Helps the pH/EC model account for plant stress, evaporation, and irrigation demand between sparse lab samples.
03
Prediction Use Case
Forecast-driven fertigation decision
1
Measure
manual pH/EC at t0
2
Forecast
predict pH/EC for 48h
3
Evaluate risk
compare with optimal range
4
Adjust
water, fertilizer, or acid timing
Goal: keep pH and EC near the optimal range between lab samples.
02
01
04